Red F: 208.96.48.0/24
Network: 208.96.48.0/24
HostMin: 208.96.48.1
HostMax: 208.96.48.254
Broadcast: 208.96.48.255
Netmask: 255.255.255.0
Hosts/Net: 254

Red C: 208.96.49.0/24
Network: 208.96.49.0/24
HostMin: 208.96.49.1
HostMax: 208.96.49.254
Broadcast: 208.96.49.255
Netmask: 255.255.255.0
Hosts/Net: 254

Red A: 208.96.50.0/24
Network: 208.96.50.0/24
HostMin: 208.96.50.1
HostMax: 208.96.50.254
Broadcast: 208.96.50.255
Netmask: 255.255.255.0
Hosts/Net: 254

Red G: 208.96.51.0/24
Network: 208.96.51.0/24
HostMin: 208.96.51.1
HostMax: 208.96.51.254
Broadcast: 208.96.51.255
Netmask: 255.255.255.0
Hosts/Net: 254

Red E: 208.96.52.0/25
Network: 208.96.52.0/25
HostMin: 208.96.52.1
HostMax: 208.96.51.126
Broadcast: 208.96.52.127
Netmask: 255.255.255.128
Hosts/Net: 126

Red H: 208.96.52.128/25
Network: 208.96.52.128/25
HostMin: 208.96.52.129
HostMax: 208.96.51.254
Broadcast: 208.96.52.255
Netmask: 255.255.255.128
Hosts/Net: 126

Red D: 208.96.53.0/28
Network: 208.96.53.0/28
HostMin: 208.96.53.1
HostMax: 208.96.53.14
Broadcast: 208.96.53.15
Netmask: 255.255.255.240
Hosts/Net: 14

Red B: 208.96.53.16/28
Network: 208.96.53.16/28
HostMin: 208.96.53.17
HostMax: 208.96.53.22
Broadcast: 208.96.53.23
Netmask: 255.255.255.240
Hosts/Net: 6

Red Inter: 208.96.54.0/30 - 208.96.54.4/30 - 208.96.54.8/30 - 208.96.54.12/30 - 208.96.54.16/30 -
    208.96.54.20/30 – 208.96.54.24/30
Network: 208.96.54.0/30
HostMin: 208.96.54.1
HostMax: 208.96.54.2
Broadcast: 208.96.54.3
Netmask: 255.255.255.252
Hosts/Net: 2

--------------------------------------------------Confguración PCs--------------------------------------------------

############## PC 1 ##############
ip 208.96.48.2 255.255.255.0 208.96.48.1
save config
############## PC 2 ##############
ip 208.96.49.2 255.255.255.0 208.96.49.1
save config
############## PC 3 ##############
ip 208.96.50.2 255.255.255.0 208.96.50.1
save config
############## ROUTER 1 ##############
enable
configure terminal
interface fast 0/1
ip add 208.96.48.1 255.255.255.0
no shut
exit
interface fast 0/0
ip add 208.96.54.1 255.255.255.252
no shut
end
copy running-config startup-config
############## ROUTER 2 ##############
enable
configure terminal
interface fast 0/1
ip add 208.96.54.5 255.255.255.252
no shut
exit
interface fast 0/0
ip add 208.96.54.2 255.255.255.252
no shut
exit
interface fast 1/0
ip add 208.96.54.9 255.255.255.252
no shut
end
copy running-config startup-config
############## ROUTER 3 ##############
enable
configure terminal
interface fast 0/1
ip add 208.96.54.6 255.255.255.252
no shut
exit
interface fast 0/0
ip add 208.96.54.17 255.255.255.252
no shut
exit
interface fast 1/0
ip add 208.96.54.21 255.255.255.252
no shut
exit
interface fast 2/0
ip add 208.96.54.13 255.255.255.252
no shut
end
copy running-config startup-config
############## ROUTER 4 ##############
enable
configure terminal
interface fast 0/1
ip add 208.96.49.1 255.255.255.0
no shut
exit
interface fast 0/0
ip add 208.96.54.18 255.255.255.252
no shut
end
copy running-config startup-config
############## ROUTER 5 ##############
enable
configure terminal
interface fast 0/1
ip add 208.96.54.10 255.255.255.252
no shut
exit
interface fast 0/0
ip add 208.96.54.25 255.255.255.252
no shut
exit
interface fast 2/0
ip add 208.96.54.14 255.255.255.252
no shut
end
copy running-config startup-config
############## ROUTER 6 ##############
enable
configure terminal
interface fast 0/0
ip add 208.96.54.26 255.255.255.252
no shut
exit
interface fast 0/1
ip add 208.96.50.1 255.255.255.0
no shut
end
copy running-config startup-config
############## ROUTER 7 ##############
enable
configure terminal
interface fast 1/0
ip add 208.96.54.22 255.255.255.252
no shut
end
copy running-config startup-config

########################### OSPF ###########################
############## ROUTER 1 ##############
configure terminal
router ospf 1
network 208.96.48.0 0.0.0.255 area 1
network 208.96.54.0 0.0.0.3 area 1
passive-interface fastEthernet 0/1
end
############## ROUTER 2 ##############
configure terminal
router ospf 1
network 208.96.54.0 0.0.0.3 area 1
network 149.224.54.4 0.0.0.3 area 0
network 149.224.54.8 0.0.0.3 area 0
end
############## ROUTER 3 ##############
configure terminal
router ospf 1
network 208.96.54.4 0.0.0.3 area 0
network 208.96.54.12 0.0.0.3 area 0
network 208.96.54.16 0.0.0.3 area 2
network 208.96.54.20 0.0.0.3 area 4
end
############## ROUTER 4 ##############
configure terminal
router ospf 1
network 208.96.54.16 0.0.0.3 area 2
network 208.96.49.0 0.0.0.255 area 2
passive-interface fastEthernet 0/1
end
############## ROUTER 5 ##############
configure terminal
router ospf 1
network 208.96.54.8 0.0.0.3 area 0
network 208.96.54.12 0.0.0.3 area 0
network 208.96.54.24 0.0.0.3 area 3
end
############## ROUTER 6 ##############
configure terminal
router ospf 1
network 208.96.54.24 0.0.0.3 area 3
network 208.96.50.0 0.0.0.255 area 3
end
############## ROUTER 7 ##############
configure terminal
router ospf 1
network 208.96.54.20 0.0.0.3 area 4
end